## Slide 1: EEG-based Mind Reading IV. SSVEP BCI Data Analysis
Yijun Wang, PhD
Institute of Semiconductors, Chinese Academy of Sciences
wangyj@semi.ac.cn
2018 IEEE EMBS International Summer School, August 13-17, 2018 Beijing, China

## Slide 2: Data and Scripts
Data files:
S1.mat, S2.mat, … , S10.mat
Matlab Scripts:
AMP_SNR_demo.m
FBCCA_demo.m
FFT_demo.m
ITCCA_demo.m
itr.m
ITR_demo.m
STDCCA_demo.m
Combination_demo.m
References:
CCA_JNE09.pdf
Combination_PNAS15.pdf
Dataset_IEEETNSRE17.pdf
FBCCA_JNE15.pdf
ITCCA_PONE15.pdf
ITR
Amplitude Spectrum and SNR
FFT-based SSVEP detection
CCA-based SSVEP detection
FBCCA-based SSVEP detection
ITCCA-based SSVEP detection
Combination method?

## Slide 3: Information transfer rate (ITR)
% function [ itr ] = itr(n, p, t)
%
% Input:
% n : # of targets
% p : Target identification accuracy (0 <= p <= 1)
% t : Averaged time for a selection [s]
N: number of classes
P: accuracy
T: selection time (seconds/selection)
Bits/min
Walpaw et al. 2002
Open: itr.m

## Slide 4: Information transfer rate (ITR)
% Examples of ITR calculation
t=2;%time per selection
p=0:0.1:1;%accuracy
for k=1:length(p)
itr32(k)=itr(32,p(k),t);
itr16(k)=itr(16,p(k),t);
itr4(k)=itr(4,p(k),t);
end
figure;
plot(p*100,itr32,'b');
hold on
plot(p*100,itr16,'k');
plot(p*100,itr4,'r');
xlabel('Accuracy (%)')
ylabel('ITR (bpm)')
Run: ITR_demo.m

## Slide 5: Data description
https://pan.baidu.com/s/1qYhyLtE

## Slide 6: Data description
An offline BCI experiment with cue-guided target selection
The experiment consisted of 6 blocks, each containing 40 trials corresponding to all 40 characters indicated in a random order. Each trial lasted 6 s in total.
(1) Each trial started with a 0.5-s target cue (a red square at the target location, the same size as the stimulus).
(2) Subjects were asked to shift their gaze to the target as soon as possible.
(3) After the cue, all stimuli started to flicker on the screen concurrently for 5 s.
(4) The screen was blank for 0.5 s before the next trial began.

## Slide 7: Data description
freq = [8:1:15 8.2:1:15.2 8.4:1:15.4 8.6:1:15.6 8.8:1:15.8];
nCondition = 40;
channels = [1:9];% Pz, PO5, PO3, POz, PO4, PO6, O1, Oz, and O2
nChannel = length(channels);
rfs = 250;% sampling rate
dataLength = 6*rfs;% [-0.5 5.5s]
nBlock = 6;% six blocks
latencyDelay = 0.5*rfs+35;% 140ms delay
Stimulus Onset
Stimulus Offset
5s
0.5s
0.5s

## Slide 8: Data description
Data for 10 subjects (*.mat files)
S1, S2, S3, S4, S5, S6, S7, S8, S9, S10
>>load S1.mat
>>size(data)
ans =
9 1500 40 6
>>plot([1:1500]/250,data(8,:,1,1))
>> xlabel('Time (s)')
>> ylabel('Amplitude (uV)')
Channels
Time points
Classes
Trials

## Slide 9: Data description
>> vep=data(8,128+35+1:128+35+250*5,3,1);
>> amp=abs(fft(vep))/(length(vep)/2);
>> plot(([1:5*250]-1)/5,amp)
>> xlim([0 50])
>> xlabel(‘Frequency (Hz)')
>> ylabel(‘Amplitude (uV)')
FFT:
Data length = 5 seconds;
Frequency resolution = 1/5=0.2Hz.
Extract vep epoch (Oz, 10Hz, trial 1)

## Slide 10: Amplitude Spectrum and SNR
Run: AMP_SNR_demo.m
% predefined bandpass filter
fs = rfs/2;
Wp=[6/fs 90/fs];%6-90Hz
Ws=[4/fs 100/fs];%
[k,Wn]=cheb1ord(Wp,Ws,3,40);
[B,A] = cheby1(k,0.5,Wn);
Line 19-24: bandpass filter

## Slide 11: Amplitude Spectrum and SNR
Run: AMP_SNR_demo.m
n=5;%width of background neighbours [-1 +1]Hz
vepSnr=zeros(length(vepAmp));
f1=6;%SNR starts from f1 Hz
for k=f1*sTime+1:length(vepAmp)-n
vepSnr(k)=20*log10(vepAmp(k)/mean(vepAmp([k-n:k-1 k+1:k+n])));%SNR
end
Line 47-52: SNR calculation

## Slide 12: Amplitude Spectrum and SNR
Run: AMP_SNR_demo.m
Line 29: iTarget=8; (15Hz)
Line 36: for sub=[1] (subject 1)

## Slide 13: FFT-based target identification
Run: FFT_demo.m
% FFT
vepFFT=abs(fft(testData,5*rfs));%5*rfs-point FFT, zero-padding
for kk = 1:nCondition
amp(kk)=mean(vepFFT(freq(kk)*5*[1:5]+1));% mean of fundamental and harmonics
end
% target identification
pLabels(ii,jj) = find(amp==max(amp));
Line 34-41: FFT and target identification
iChannel = [8];% Oz for FFT
Line 11: channel selection
stimTime = 5;% stimulation time (up to 5s)
Line 16: data length
……
Block 6 - Target 36: estimated as 11
Block 6 - Target 37: estimated as 4
Block 6 - Target 38: estimated as 38
Block 6 - Target 39: estimated as 27
Block 6 - Target 40: estimated as 19
Accuracy = 51.25%
ITR = 19.04 bpm

## Slide 14: FFT-based target identification
Run: FFT_demo.m
iChannel = [8];% Oz for FFT
Line 11: channel selection
stimTime = 5;% stimulation time (up to 5s)
Line 11: Oz(8), Line 16: data length
Accuracy = 51.25%
ITR = 19.04 bpm
8-Oz
Accuracy = 52.08%
ITR = 19.53 bpm
7-O1
Accuracy = 67.08%
ITR = 29.11 bpm
9-O2
Accuracy = 51.25%
ITR = 19.04 bpm
5s
Accuracy = 47.50%
ITR = 20.65 bpm
4s
Accuracy = 32.50%
ITR = 20.27 bpm
2s

## Slide 15: FFT-based target identification
Run: FFT_demo.m
Line 16: 5 seconds; Line 37: number of harmonics ([1:5])
Accuracy = 51.25%
ITR = 19.04 bpm
1:5
Accuracy = 50.83%
ITR = 18.80 bpm
1:4
Accuracy = 48.75%
ITR = 17.60 bpm
1:3
amp(kk)=mean(vepFFT(freq(kk)*5*[1:5]+1));% mean of fundamental and harmonics
Accuracy = 39.17%
ITR = 12.44 bpm
1:2
Accuracy = 17.92%
ITR = 3.33 bpm
1:1

## Slide 16: FFT-based target identification
Run: FFT_demo.m
load(['S1.mat']);
Line 37: [1:5], Line 22: subject index
Accuracy = 51.25%
ITR = 19.04 bpm
S1
Accuracy = 71.25%
ITR = 32.04 bpm
S2
Accuracy = 93.75%
ITR = 50.77 bpm
S10
Accuracy = 99.17%
ITR = 56.82 bpm
S3
…

## Slide 17: CCA-based target identification
Run: STDCCA_demo.m
% reference signals for CCA
for ii = 1:length(freq);
s1 = sin(2*pi*freq(ii)*t);
s2 = cos(2*pi*freq(ii)*t);
…
s9 = sin(2*pi*5*freq(ii)*t);
s10 = cos(2*pi*5*freq(ii)*t);
refData(:,:,ii) = cat(2,s1',s2',s3',s4',s5',s6',s7',s8',s9',s10');
end
figure;
for i=1:10
subplot(10,1,i);plot(t,refData(:,i,3));
end
Line 19-36: sinusoidal reference signals
10Hz

## Slide 18: CCA-based target identification
Run: STDCCA_demo.m
% CCA
for kk = 1:nCondition
[~,~,D] = canoncorr(testData, refData(:,:,kk));
cc(kk)=D(1);
end
% target identification
pLabels(ii,jj) = find(cc==max(cc));
Line 65-72: CCA and target identification

## Slide 19: CCA-based target identification
Run: STDCCA_demo.m
Accuracy = 51.25%
ITR = 19.04 bpm
S1
Accuracy = 71.25%
ITR = 32.04 bpm
S2
Accuracy = 93.75%
ITR = 50.77 bpm
S10
Accuracy = 99.17%
ITR = 56.82 bpm
S3
…
load(['S1.mat']);
Line 48: subject index
Accuracy = 93.75%
ITR = 50.77 bpm
FFT
CCA
Accuracy = 100.00%
ITR = 58.06 bpm
Accuracy = 100.00%
ITR = 58.06 bpm
Accuracy = 99.58%
ITR = 57.39 bpm
FFT
CCA

## Slide 20: CCA-based target identification
Run: STDCCA_demo.m
nHarmonics=5;
Line 37: number of harmonics
Accuracy = 93.75%
ITR = 50.77 bpm
5
Accuracy = 93.75%
ITR = 50.77 bpm
3
Accuracy = 90.83%
ITR = 47.95 bpm
1
5s
Accuracy = 71.25%
ITR = 70.49 bpm
5
Accuracy = 69.58%
ITR = 67.87 bpm
3
Accuracy = 57.50%
ITR = 50.21 bpm
1
2s
stimTime = 5;% stimulation time (up to 5s)
Line 15: data length
Line 48: subject index (‘S1’)

## Slide 21: FBCCA-based target identification
Run: FBCCA_demo.m
% predefined bandpass filters for a filter bank
fs = rfs/2;
%h1
fls1(1) = [6]; fls2(1) = [4];
fhs1(1) = [90]; fhs2(1) = [100];
…
%h7
fls1(7) = [54]; fls2(7) = [48];
fhs1(7) = [90]; fhs2(7) = [100];
for nFB=1:7
Wp=[fls1(nFB)/fs fhs1(nFB)/fs];%
Ws=[fls2(nFB)/fs fhs2(nFB)/fs];%
[k,Wn]=cheb1ord(Wp,Ws,3,40);
[B{nFB},A{nFB}] = cheby1(k,0.5,Wn);
end
Line 36-79: filter bank
Sub Band | Lower Freq (Hz) | Upper Freq (Hz)
1 | 6 | 90
2 | 14 | 90
3 | 22 | 90
4 | 30 | 90
5 | 38 | 90
6 | 46 | 90
7 | 54 | 90

## Slide 22: FBCCA-based target identification
Run: FBCCA_demo.m
% standard CCA for all sub-bands
for kk = 1:nCondition
[~,~,D] = canoncorr(testDatah1, refData(:,:,kk));
cc(1,kk)=D(1);
……
[~,~,D] = canoncorr(testDatah7, refData(:,:,kk));
cc(7,kk)=D(1);
end
% weighted sum
rrr = weights(1:nSubband)*cc(1:nSubband,:).^2;
% target identification
pLabels(ii,jj) = find(rrr==max(rrr));
Line 111-133: FBCCA and target identification
weights = [1:7].^(-1.25)+0.25;
Line 15: weights

## Slide 23: FBCCA-based target identification
Run: FBCCA_demo.m
Accuracy = 51.25%
ITR = 19.04 bpm
5s
Accuracy = 32.50%
ITR = 20.27 bpm
2s
Accuracy = 20.83%
ITR = 15.97 bpm
1s
FFT
stimTime = 5;% stimulation time (up to 5s)
Line 16: data length
Accuracy = 93.75%
ITR = 50.77 bpm
Accuracy = 71.25%
ITR = 70.49 bpm
Accuracy = 42.50%
ITR = 51.96 bpm
CCA
Accuracy = 99.58%
ITR = 57.39 bpm
Accuracy = 92.50%
ITR = 108.99 bpm
Accuracy = 65.42%
ITR = 102.55 bpm
FBCCA

## Slide 24: FBCCA-based target identification
Run: FBCCA_demo.m
Accuracy = 92.50%
ITR = 108.99 bpm
7
Accuracy = 92.92%
ITR = 109.88 bpm
6
Accuracy = 91.25%
ITR = 106.35 bpm
5
nSubband = 7;% number of subbands
Line 19: number of subbands
Accuracy = 91.25%
ITR = 106.35 bpm
Accuracy = 85.42%
ITR = 94.84 bpm
Accuracy = 79.58%
ITR = 84.30 bpm
Accuracy = 71.25%
ITR = 70.49 bpm
4
3
2
1
CCA
2s

## Slide 25: ITCCA-based target identification
Run: ITCCA_demo.m
% leave-one-out training data
rawData1=rawData;
rawData1(:,:,:,ii)=[];
trainData(:,:,:)=mean(rawData1,4);
for jj=1:nCondition
for chan = 1:nChannel
refData(chan,:,jj) = trainData(chan,1:N+latencyDelay,jj);
refDatah1(chan,:,jj) = filtfilt(B{1},A{1},refData(chan,:,jj));
…….
refDatah7(chan,:,jj) = filtfilt(B{7},A{7},refData(chan,:,jj));
end
end
Line 71-86: individual template
Y: SSVEP templates

## Slide 26: ITCCA-based target identification
Run: ITCCA_demo.m
% IT-CCA for all sub-bands
for kk = 1:nCondition
refTmph1 = refDatah1(:,1+latencyDelay:N+latencyDelay,kk)';
[SFA,SFB,D] = canoncorr(testDatah1,refTmph1);
cc(1,kk)=corr2(testDatah1*SFA(:,1),refTmph1*SFA(:,1));
……
refTmph7 = refDatah7(:,1+latencyDelay:N+latencyDelay,kk)';
[SFA,SFB,D] = canoncorr(testDatah7,refTmph7);
cc(7,kk)=corr2(testDatah7*SFA(:,1),refTmph7*SFA(:,1));
end
% weighted sum
rrr = weights*(sign(cc).*cc.^2);
% target identification
pLabels(ii,jj) = find(rrr==max(rrr));
Line 112-148: ITCCA and target identification

## Slide 27: ITCCA-based target identification
Run: ITCCA_demo.m
Accuracy = 51.25%
ITR = 19.04 bpm
5s
Accuracy = 32.50%
ITR = 20.27 bpm
2s
Accuracy = 20.83%
ITR = 15.97 bpm
1s
FFT
stimTime = 5;% stimulation time (up to 5s)
Line 16: data length
Accuracy = 93.75%
ITR = 50.77 bpm
Accuracy = 71.25%
ITR = 70.49 bpm
Accuracy = 42.50%
ITR = 51.96 bpm
CCA
Accuracy = 99.58%
ITR = 57.39 bpm
Accuracy = 92.50%
ITR = 108.99 bpm
Accuracy = 65.42%
ITR = 102.55 bpm
FBCCA
Accuracy = 98.33%
ITR = 55.76 bpm
Accuracy = 99.58%
ITR = 126.26 bpm
Accuracy = 95.83%
ITR = 194.07 bpm
ITCCA

## Slide 28: ITCCA-based target identification
Run: ITCCA_demo.m
Accuracy = 95.83%
ITR = 194.07 bpm
6
Accuracy = 94.00%
ITR = 187.09 bpm
5
Accuracy = 92.50%
ITR = 181.65 bpm
4
nBlock = 6;% six blocks
Line 16: 1 second; Line 13: number of training trials (nBlock-1)
Accuracy = 85.00%
ITR = 156.77 bpm
Accuracy = 55.00%
ITR = 78.03 bpm
3
2
1s

## Slide 29: Summary
 | Year | Number of channels | Number of harmonics | Number of sub-bands | Number of training trials | Accuracy (%) | ITR (bpm)
FFT | 2002 | 1 | 5 | 1 | 0 | 20.83% | 15.97
CCA | 2007 | 9 | 5 | 1 | 0 | 42.50% | 51.96
FBCCA | 2015 | 9 | 5 | 7 | 0 | 65.42% | 102.55
ITCCA | 2014 | 9 | - | 7 | 5 | 95.83% | 194.07
Subject S1 (data length: 1 s)

## Slide 30: Homework
How to combine the FBCCA method and the IT-CCA method to further improve SSVEP detection?
Use linear combination of correlation coefficients from CCA and IT-CCA to improve the detection (weights?);
For different data lengths (e.g., from 0.5s to 1s with an interval of 0.1s), calculate average accuracy and ITR (mean ± standard deviation) cross 10 subjects for FBCCA, ITCCA, and the combination method.

## Slide 31: Homework
How to combine the FBCCA method and the IT-CCA method to further improve SSVEP detection?
Submit to: wangyj@semi.ac.cn

## Slide 32: EEGLAB (https://sccn.ucsd.edu/eeglab/)
EEGLAB is an interactive Matlab toolbox for processing continuous and event-related EEG, MEG and other electrophysiological data incorporating ICA, time/frequency analysis, artifact rejection, event-related statistics, and visualization of the averaged and single-trial data.

## Slide 33: Thanks for your attention!